## Slide 1: CS++ - The successor of the CS Framework
Live-Demonstration eines Aktor-basierten Powersupplies
Dr. Holger Brand, GSI Helmholtzzentrum für Schwerionenforschung GmbH

## Slide 2: Content
CS Framework
  Innovation CS → CS++
NI Actor Framework
CS++
  Base Classes & Factory
    CS++Base & CS++Reference; CS++BaseActor
  Configuration
  CS++StartActor
  CS++DeviceActor
    CS++DMM, CS++DCPwr
  CS++GUIActor
    CS++DeviceGUIActor; CS++DCPwrGui
  Build Specification

## Slide 3: CS Framework I
CS is a framework that can be used by many experiments.
CS is a
  multi-threaded,
  event driven,
  object oriented and
  distributed framework with
  SCADA functionality.
An experiment control system can be developed by combining the CS framework with experiment specific add-ons.
CS is supported on MS-Windows and Linux
  LabVIEW RT on Pharlab
Lasers
Ion Traps
Nuclear Physics Experiments

## Slide 4: CS Framework II
Development was started with LabVIEW 6
  On top of ObjectVIEW, Vogel Automatisierungstechnik (ObjectVIEW was removed with CS 2.0)
Artificial object-oriented approach
  Inspired by C++
    by reference
    multiple inheritance
  DIM as core for the network communication (CS 3.0)
    Publisher-Subscriber-Pattern (one to many)
    Command-Pattern (many to one)
  Many things rely on design recommendations and can not be enforced.

## Slide 5: CS Framework III
Base classes
  CSObj -> Object reference & Attributes
  CAEObj -> Capabilities for active threads and events (DIM)
  BaseGUI -> Graphical User Interface, adds an active thread
  BaseSM -> State Machine, adds an active thread
  BaseProcess -> Adds threads for concrete event-handling and periodic actions

## Slide 6: CS Framework IV
SuperProcess
  Watchdog functionality & Process maintenance
  Can automatically launch more processes during startup.
DSCIntProc
  Provides connectivity to the Data Logging & Supervisory Control Module (DIM <-> Tags, Shared Variables)
  Alarming, Trending
  IO-Server like OPC, EPICS etc.
Configuration Database
  Object configuration data
    Watchdog timeouts
    VISA Resource etc.
  Mass configuration

## Slide 7: CS Framework V

## Slide 8: Innovation: CS → CS++
LVOOP, Native object-oriented support by LabVIEW
Feasibility study: Mobile Agents was successful.
CS++ respecting dataflow
  Similar requirements as CS Framework
  Less complexity
    Enable short-term students to join
  Enforce recommendations by LVOOP properties.
  Based on NI Actor Framework
    Part of LabVIEW since 2012
    Long term support by NI
    Profit from the community
Driving project is the test facility for the superconducting SIS-100 Dipole Magnets at FAIR.

## Slide 9: NI Actor Framework I Stephen R. Mercer et al. @ NI Week 2011
Standard approach
  Queued State Machine
  Modular & Event-driven
  But, scaling is a problem!

## Slide 10: NI Actor Framework II Stephen R. Mercer et al. @ NI Week 2011
Override
Extend
Decorate
Three Sources of Code Replication
  Override the handling of one message
  Extend the set of handled messages
  Decorate the machine with additional behavior
LVOOP
  Cluster & Node -> Class & Methode
  Message & Case Structure -> Class & Dynamic Dispatch

## Slide 11: CS++ Base Classes
Classes representing passive data are derived from LabVIEWObject, the ultimate LabVIEW ancestor class.
CS++Base.lvclass inherits from LabVIEWObject
  To be used as ancestor class for objects to be treated as entity.
  Can be referenced using the CS++Reference.lvclass (LV-Reference Pattern is assumed to be well known.)
CS++BaseActor.lvclass inherits from Actor
  To be used as ancestor class for actors part of CS++.
  It provides common features that all CS++Actors should have.
    Dynamic dispactch VIs: Initialize Attributes.vi, After Launch Init.vi
CS++Factory inherits from LabVIEWObject
  To be used to dynamically create initialized objects
    CS++Base & CS++BaseActor.
  Configuration data is read from ini-file by default and
  provided to the object as Variant for attribute initialization.
    Derived factories can read from database etc.

## Slide 12: CS++ Class Hierarchie

## Slide 13: Example Configuration
[CS++StartActor]
LVClassPath="C:\...\CSPP\Core\Actors\CS++StartActor\CS++StartActor.lvclass"
LVLibPath="C:\...\CSPP\Core\Actors\CS++StartActor\CS++StartActor.lvlib"
CS++StartActor:CS++StartActor.MessageLogger="Syslog"
CS++StartActor:CS++StartActor.Open_ActorCore=True
[Syslog]
// Can be loaded from the labVIEW Tools Network
IP="140.181.78.202"
Port=514
Debug=True
[CS++StartActor.StartActors]
#Actor Object to start with option to open its Actor Core.vi.
mySVClient=True
myDSCTrending=True
myDSCAlarmViewer=True
myCS++DeviceActor=False
myDMM=False
myDCPwr=False

## Slide 14: CS++Factory.CreateObject
dynamic dispatch
next transparency

## Slide 15: CS++StartActor.Initialize Attributes
Call parent method.
Read initialization data from Variant.
  Specify default values
Save to object attribute data.
Check if data was found.

## Slide 16: Launch CS++StartActor
Load class constants,
include dependencies
for building application
Parse command line parameters
Launch Start-Actor
→ dispatch Actor Core.vi
→ Message Handling
Close launching VI

## Slide 17: Actor.lvclass:Actor Core.vi

## Slide 18: CS++BaseActor: Attributes and Methods
Initialize Attributes.vi
Actor Core.vi: send After Launch Init.vi
Resources should be allocated after activation.
Stop Core.vi
Release allocated resources.
Pre Launch Init.vi e.g. check conditions that may hinders activating the actor.

## Slide 19: CS++BaseActor:Handle Error.vi
Actor Core will stop execution by default in case of error as result of message handling.
CS++BaseActor will send the error info to the message logger.
Derived classes need to override this method if stopping is not an adequate reaction!

## Slide 20: CS++BaseActor:Messages
After Launch Init Msg.lvclass
  Dynamich dispatch After Launch Init.vi: Allocate resources here.
Open Core FP Msg.lvclass
  Open or close the frontpanel of the Actor Core.vi.
Launch GUI Msg.lvclass
  Trigger an actor to launch an associated GUI actor.

## Slide 21: 3-Tier Architecture
Shared Variable Engine
Device Layer
GUI Layer
Control Layer
Network
Message1
1Linked Network Actor

## Slide 22: CS++DeviceActor.lvclass & Configuration
[myDeviceActor]
LVClassPath="C:\...\CSPP\Core\Actors\CS++DeviceActor\CS++DeviceActor.lvclass"
LVLibPath="C:\...\CSPP\Core\Actors\CS++DeviceActor\CS++DeviceActor.lvlib"
CS++DeviceActors:CS++DeviceActor.ResourceName="COM1"
CS++DeviceActors:CS++DeviceActor.Reset=False
CS++DeviceActors:CS++DeviceActor.Selftest=True
CS++DeviceActors:CS++DeviceActor.OptionString=""
CS++DeviceActors:CS++DeviceActor.ResetWithDefaults=False
CS++DeviceActors:CS++DeviceActor.PollingInterval_s=10.
CS++BaseActor:CS++BaseActor.DefaultGUI=“C:\...\CS++DeviceGUIActor.lvclass"
CS++BaseActor:CS++BaseActor.LaunchDefaultGUI=True
PV-URL are defined in a separate section, so it can be used by other objects, too, e.g. the corresponding GUI.
[myDeviceActor.URLs]
ResourceName="ni.var.psp://localhost/myProcess/myDeviceActor_ResourceName"
DriverRevision="ni.var.psp://localhost/myProcess/myDeviceActor_DriverRevision"
FirmwareRevision="ni.var.psp://localhost/myProcess/myDeviceActor_FirmwareRevision"
SelftestResultCode="ni.var.psp://localhost/myProcess/myDeviceActor_SelftestResultCode"
SelftestResultMessage="ni.var.psp://localhost/myProcess/myDeviceActor_SelftestResultMessage"
ErrorCode="ni.var.psp://localhost/myProcess/myDeviceActor_ErrorCode"
ErrorMessage="ni.var.psp://localhost/myProcess/myDeviceActor_ErrorMessage"

## Slide 23: CS++DeviceActor.After Launch Init.vi

## Slide 24: CS++DeviceActor.Initialize Device.vi

## Slide 25: CS++DeviceGUIActor.lvclass
Pre Launch Init.vi
  Read URLs from configuration file
  For URLs corresponding to static PVs
    Open PV Connection
    Read PV once and store in object attibutes
    Close PV Connection
Actor Core.vi
  For URLs corresponding to dynamic PVs
    Register PVs with Update-Message to PVMonitor-Actor
  Register corresponding dynamic GUI events.

## Slide 26: CS++DeviceGUIActor.Actor Core.vi I

## Slide 27: CS++DeviceGUIActor.Actor Core.vi II

## Slide 28: CS++PVMonitor
Implementation for Shared Variable
  Periodic reading of shared variable values
  Send registered Update-Messages to observers

## Slide 29: Live Demonstration
Demo of existing classes
Live implementation of a DC Power Supply actor class
  derived from CS++DCPwr.lvclass

## Slide 30: References
CS Framework, http://wiki.gsi.de/cgi-bin/view/CSframework/WebHome
DIM, http://dim.web.cern.ch/dim
LVOOP
  The Decisions Behind the Design, http://zone.ni.com/devzone/cda/tut/p/id/3574
  FAQ, http://zone.ni.com/devzone/cda/tut/p/id/3573
  Common OO Design Patterns for LabVIEW, http://decibel.ni.com/content/docs/DOC-2875
  Mobile Agent System, http://wiki.gsi.de/cgi-bin/view/NIUser/LVMobileAgentSystem
    Diploma Thesis of Frederik Berck, http://wiki.gsi.de/pub/NIUser/LVMobileAgentSystem/DiplomarbeitFrederikBerck.pdf
NI Actor Framework
  Community@NI, https://decibel.ni.com/content/groups/actor-framework-2011?view=overview
  READ THIS FIRST to get started with Actor Framework, https://decibel.ni.com/content/docs/DOC-17193
  Actor Framework.pptx at NI Week 2011, https://decibel.ni.com/content/docs/DOC-17109
CS++
  Published on GitHub, https://github.com/HB-GSI/CSPP, License: EUPL v1.1

## Slide 31: Command Pattern
http://en.wikipedia.org/wiki/Command_Pattern